## Slide 1: Introduction to Water, Sanitation and Hygiene in Schools

## Slide 2: What is it?
Provision of safe drinking water
Management of excretion
Adoption of good hygienic behaviour

## Slide 3: Snapshot

## Slide 4: Water
1.1 billion people worldwide do not have access to safe drinking water
Nearly two million children die each year due to diarrhoea and other infectious diseases resulting from unsafe drinking water
12% increase in attendance in Tanzania when water sources were within 15 minutes from the school rather than over an hour

## Slide 5: Water uses in Schools
Drinking
Food preparation
Washing of utensils
Hand washing
Cleaning
Flushing
Priority

## Slide 6: Sources - Ground Water
Borehole
    Pro’s – Cleanest – Generally non-seasonal
    Con’s – High capital/operating costs – Highly technical (pump required)
Well
    Pro’s – Cheap (community construction/maintenance) – low tech
    Con’s – Open to contamination – possible seasonal supply
Spring
    Pro’s – Very cheap (little construction requirements) – no tech – reduced chances of contamination
    Con’s – Mostly seasonal – location is naturally occurring

## Slide 7: Example – Borehole

## Slide 8: Spot the problems

## Slide 9: Example - Well

## Slide 10: Example - Spring

## Slide 11: Source – Surface Water
Lakes
    Pro’s – No expense
    Con’s – Stagnated – Disease Breeding Ground – Seasonal – Used for washing – Locality
River
    Pro’s – No expense - Less stagnated than lakes
    Con’s – Disease Breeding Ground – Seasonal – Used for washing – Locality
Roof water harvesting
    Pro’s – Locality – Reduced contamination from washing etc
    Con’s – Incurs a cost – requires maintenance

## Slide 12: Lake

## Slide 13: River

## Slide 14: Roof water harvesting

## Slide 15: Treatment
Disinfectant
    Chlorine
    Kills most bacteria, viruses and amoeba
    Provides 24 hr protection
    Relatively cheap
Filter
    Sand Beds or Gauze
    Removes solids – heavy metals (Lead etc)
    Flocculants can be added to improve filtration (especially when filtering with gauze)

## Slide 16: Example – Filtration

## Slide 17: Considerations
Location – Publically accessible
Design – Relating to local needs and setting
Cost – Capital/Operation/Maintenance (Recovery)
Management – Responsibility for cleaning, use and repair
Training – End users and managers
Cultural norms – who collects water - odur

## Slide 18
CAUTION CLEAN WATER NEEDS TO BE PROTECTED
!

## Slide 19: Disposal of excretion
Worms in most cases are sourced through poor excretion management
Many schools in rural Sub-Saharan Africa do not have sufficient or adequate latrine facilities
Children forced to defecate in and around the school compound + School Feeding ↑ problem
11% increase in girls enrolment in Bangladesh when suitable latrines were present

## Slide 20: The Latrine
Varies in complexity and cost
Offers a place of privacy
Contains excretion in one place
Allows for management of excretion

## Slide 21: Examples of Latrines
Flushing toilet
    Pro’s – very clean – offers opportunities for foul water treatment – very little smell
    Con’s – expensive – high water demand – need for addition equipment (Septic tank) or requires municipal connection – high technical maintenance requirement – NOT REALISTIC IN RURAL SETTINGS
Pit latrine
    Pro’s – Cheap – Easily constructed – Low tech maintenance
    Con’s – No opportunity for foul water treatment – possible ground water contamination – possible smell

## Slide 22: Example – Pit Latrine
NGL
NGL
1’-6”
6’- 6”
6’- 0”
8’
4’- 7.5”
3’- 0”
9” thick Brick wall
Earth Filling
1’- 9”
4.5” thick Brick walling
5’- 6”

## Slide 23: Considerations
Location – Safe – away from school
Design – Relating to gender, local needs and setting
Cost – Capital/Operation/Maintenance (Recovery)
Management – Responsibility for cleaning, use and repair
Training – End users and managers

## Slide 24: Hygienic Behaviour
Promoting the adoption of safer hygienic practices
Reducing the spread of germs
How
  Wash your hands with soap frequently (after using the toilet – before eating)
  Stay home if you are sick
  Cover your nose and mouth when sneezing and coughing
  Wash your hands after coughing, sneezing
  Do not share cups, glasses, dishes or cutlery

## Slide 25: Creating behavioural change is not easy The process maybe long and complex

## Slide 26: Achieving behavioural change
Education
    Training school children and teachers on improved hygienic behaviour (Soap making/hand washing)
    Awareness campaigns
Infrastructure
    Ensure hand facilities are available
Empowerment
    Include end users in designing facilities and managing there use
    Creating school WASH clubs (Child – Child learning)

## Slide 27: Education – Infrastructure – Empowerment

## Slide 28: Considerations for a WASH programme
Selecting the school
    Readiness of the community (strong existing relationship)
    Existing school infrastructure (Needs basis)
    Engagement with local authorities
Making a plan
    Using various participatory methods exit
    Should include end users, teachers, community, professionals and local authorities
    Includes management structures as well as infrastructure
Funding
    Contribution from parents
    Using school maintenance budget
    Income generating opportunities
Monitoring
    Check list developed by students
    Frequent reports created

## Slide 29: Thank You